◎ 第1題為選擇題，請於答案卷對應空格填入選項。2-8題為計算或問答題，需寫明過程。

- Choose one right answer for each of the following questions. (10%)

- The diodes in a bridge rectifier each have a maximum dc current rating of 2A. This means the dc load current can have a maximum value of

(A) 1A  (B) 2A  (C) 4A  (D) 8A

- The device associated with voltage-controlled capacitance is a

(A) Light-emitting diode  (B) Photodiode  (C) Varactor diode  (D) Zener diode

- Increasing the collector supply voltage will increase

(A) Base current  (B) Collector current  (C) Emitter current  (D) None of the above

- If the base resistor has zero resistance, the transistor will probably be

(A) Saturated  (B) In cutoff  (C) Destroyed  (D) None of the above.

- With CMOS, the upper MOSFET is

(A) A passive load  (B) An active load  (C) Nonconducting  (D) Complementary

- Show that the series connection of MOSFETs shown in Fig. 1 behaves as a single MOSFET with Twice the length of the individual MOSFETs. (Neglect the body effect) (10%)

Fig. 1

- Show that the parallel connection of MOSFET shown in Fig. 2 behaves as a single MOSFET a width equal to the sum of the individual MOSFET’s widths. (10%)

Fig. 2

- What would happen to the transfer function analysis results for the circuit in Fig. 3? (10%)

(a) A capacitor is added in series with R1. Why?

(b) A capacitor is added in series with R2. Why?

Fig. 3

- Describe the transfer characteristic of the circuits shown in Fig. 4 (a) and (b). (10%)

Fig. 4

- An OPA circuit is shown in Fig. 5. (10%)

(a) Find VO and CMRR.

(b) How to set R1~ R4 for converting the circuit to differential amplifier?

Fig. 5

- Fig. 6 shows a circuit for charging a 12-V battery. If vs is a sinusoid with 24-V peak amplitude, find the fraction of each cycle during which the diode conducts. Also find the peak value of the diode current and the maximum reverse-bias voltage that appears.	(20%)

Fig. 6

- Explain the following terms. (20%)

(1) Can you set up a lighting source by only using LED diodes without any rectifier circuits (that is 110-V AC LED)?

(2) What is the field effect in MOSFET? And what is the meaning of Vt of MOSFET? Sketch the structure and explain it.

(3) Design a Constant-Current Source for biasing using two BJT and show the current.

(4) Explain Frequency Compensation by using Bode plots.

# Text boxes

國立臺南大學 101學年度  電機工程學系碩士班  招生考試  電子學  試題卷