- The reaction, 2NO + O2 ( 2NO2, was believed to occur the following mechanism,

2NO  (  N2O2           (1)

N2O2  (  2NO                 (2)

N2O2 + O2  (  2NO2          (3)

Assuming N2O2 is intermediate and steady state, (a) Derive the rate equation. (b) Under what conditions, does the rate equation reduce to second-order kinetics in NO and first-order kinetics in O2? Which mechanism will be the rate determining step?    (15 points)

- For the decomposition A ( R, CA0 = 1 mol/liter, in a batch reactor conversion is 75 % after 1 hour, and is just complete after 2 hours. Find a rate equation to represent this kinetics.    (5 points)

- Consider the parallel decomposition of A of different orders:    (30 points)

S is the desired product and CA0 = 4. Determine the maximum concentration of desired product obtainable in (a) PFR, (b) MFR, (c) the best combination of PFR and MFR.

- Fifty kmol/hr of air is compressed from P1=1.2 bar to P2=6.0 bar in a steady-flow compressor. Delivered mechanical power is 98.8 kW. Temperatures and velocities are: T1=300 K, T2=520 K; u1=10 m/s, u2=3.5 m/s. Estimate the rate of heat transfer from the compressor. Assume for air that Cp=(7/2)R and that enthalpy is independent of pressure.    (10 points)

- An inventor claims to have devised a cyclic engine which exchanges heat with reservoirs at 298.15 K to 523.15 K, and which produces 0.45 kJ of work for each kJ of heat extracted from the hot reservoir. Is the claim believable?    (10 points)

- For acetone at 293.15 K, 1.0 bar, ( = 1.5(10-3 K-1, ( = 60(10-6 bar-1, V = 1.3(10-3 m3 kg-1. Find:

- The value of .    (5 points)

- The pressure generated when acetone is heated at constant volume from 293.15 K, 1.0 bar to 298.15 K.    (5 points)

- The volume change when acetone is changed from 293.15 K, 1.0 bar to 283.15 K, 11.0 bar.  (5 points)

- A 75 kg steel casting (Cp=0.12 kJ(kg-1(K-1) at a temperature of 800 K is quenched in 300 kg of oil (Cp=0.6 kJ(kg-1(K-1) at 70 K. If there are no heat losses, what is the change in entropy of (a) the casting, (b) the oil, and (c) both considered together?    (15 points)

# Text boxes

k1b

k1f

k2