國立嘉義大學101學年度

電子物理學系光電暨固態電子碩士班(乙組)招生考試試題

科目：電磁學

一、單選題(每題5分，共計60分)

1.當電場滿足，其背後的物理意義為何？ (A)電場沒有旋度的分量 (B)電場是靜電場	 	(C)電場是由電荷所造成		(D)以上皆是。

2.有二個相距甚遠的導體球：半徑為r且帶有淨電荷量q的A導體球及半徑為2r且帶有淨電荷量0的導體球B。用一細長的導線與兩導體球連接後，A導體球的淨電荷量為何? (A) q		(B) q/2		(C) q/3		(D) q/4。

3.帶有靜電荷的金屬球殼，其半徑1公分，與地表之間的電位差為1.5伏特，其上靜電荷量約為？(A) 0庫倫	 (B) 1庫倫 	(C) 庫倫	(D) 庫倫。

4.下列對電偶極(electric dipole)的描述為真？ (A)由兩個電量相同但電性相反的分開電荷組成 (B)由兩個電量任意但電性相反的分開電荷組成  (C)由兩個電量相同且電性相同的分開電荷組成 (D)由偶數個電量任意但電性相反的分開電荷組成。

5.將帶有電量1庫侖的點電荷由低電位移至高電位，其電位差為1伏特，約需作功？ (A)1牛頓	(B)牛頓	(C) 1焦耳	(D)焦耳。

6.通有相同方向的電流的兩平行導線會 	(A)彼此相吸	(B)彼此排斥			(C)無相吸及相斥的現象	(D)產生感應電動勢。

7.一個線圈會有自感(self inductance)其實是下列那一個定律的展現? 			(A)高斯定律	(B)法拉第定律		(C)安培定律		(D)克希荷夫定律。

8.關於電磁波所具有的動量和動量密度(使用國際標準制)，何者有誤?			   (A)動量密度 = ，其中是坡印廷向量		(B)動量的單位為 (C)動量 = 		(D)動量密度的單位為。

9.兩個平行帶電板 (面積A，距離d) 所形成的電容器(電場E 指向z方向)置於x方向的均勻磁場B中，將一電阻線沿z方向連接此兩帶電板使其放電，當放電電流流經電阻線時會受到磁力作用，求放電期間電磁場傳遞給電容器的總衝量為 (A)		(B)	(C)		(D)指向 x方向。

10.關於真空中傳播的電磁波，何者有誤? (A)波動方程式為 ，其中f是波函數，v是傳播速度  (B)波函數f必是 z-vt 的函數 (C)平面電磁波的解可寫成  (D)平面電磁波是波動方程式的唯一解。

11.太陽光經過三稜鏡會被分成七彩光的現象乃因折射率與頻率有關，此現象稱為   (A)散光 (B)色散 (C)折射 (D)像散。

12.關於可見光從空氣中打到金屬導體上，何者有誤? (A)幾乎100% 反射	(B)在金屬導體表面會有消逝波 (C)有全內反射現象 (D)當金屬導體很薄時可見光可能會穿透過去。

二、非選擇題(每題10分，共計40分)

1. Find the electric field  at a distance s from an infinite straight wire which carries a uniform line charge density .

2. As shown in Fig. 1, find the magnetic field  at a distance z above the center of a circular loop of radius R, which carry a steady current I.

Fig. 1

- A fat wire, radius a, carries a constant current I, uniformly distributed over its cross section. A narrow gap in the wire, of width w <<a, forms a parallel-plate capacitor as shown in Fig. 2. Assume the charge is zero at t = 0. Calculate the Poynting vector in the gap, as functions of the distance s from the axis and the time t.

Fig. 2

- As shown in Fig. 3, a very long solenoid of radius a, with n turns per unit length, carries a current Is. Coaxial with the solenoid, at radius b >>a, is a circular ring of wire, with resistance R. When the current in the solenoid is gradually decreased, a current Ir is induced in the ring. The Poynting vector just outside the solenoid is

.

Calculate the power delivered to the ring .  (Hint: You need to calculate an   integral and use )

# Text boxes

背面尚有試題

Fig. 3